## Slide 2: Autonomous Vehicle Controls
Week 1
Classical controls overview

## Slide 3: Table of Contents for the week
Autonomous vehicle
About the Course
Automotive Control System
System Modelling
Control System
Transient Performance
System Types
Disturbance Rejection and Tracking
PID Controller

## Slide 4: Learning objectives
In this week, we will
  Know about the autonomous vehicle industry
  Learn about the controls Systems in Automotive Vehicle
  Know how the controls react to input
  How the system responds to disturbance
  PID Controllers

## Slide 5: Autonomous Vehicle

## Slide 6: Autonomous vehicle motivation
The first major motivation started from the 2004 DARPA challenge won by Stanford.
Autonomous cars is set to add $2 trillion to US GDP through rideshare businesses and auto sales.
Notes: Image 2 -https://www.google.com/url?sa=i&url=https%3A%2F%2Fcommons.wikimedia.org%2Fwiki%2FFile%3AWaymo_self-driving_car_front_view.gk.jpg&psig=AOvVaw06CzVVnkgb9oPzi2OuCIpI&ust=1608330255615000&source=images&cd=vfe&ved=0CAIQjRxqFwoTCKCQy6OH1u0CFQAAAAAdAAAAABAD

## Slide 7: Autonomous vehicle motivation
Major OEMS such as Tesla, Ford, Volkswagen will have autonomous vehicles on production by 2022.
Autonomous ride sharing will solve urban mobility issues while reducing the number of accidents per year.

## Slide 8: What makes an Autonomous vehicle?
An autonomous car is capable of sensing its environment and operating without human involvement.
Autonomous Vehicle Software stack:
  Hardware
    Sensors
    Computing processors
  Perception
    Sensor processing
    Sensor fusion
    localization
    Mapping
  Action
    Vehicle controls
    Local Path planning
    Behavioral Decisions
Notes: Source- Pixabay
A: image 1 :https://www.google.com/url?sa=i&url=https%3A%2F%2Fwww.theverge.com%2F2020%2F3%2F4%2F21165014%2Fwaymo-fifth-generation-self-driving-radar-camera-lidar-jaguar-ipace&psig=AOvVaw1iKk7iu1pfGiwHJ9Lo9PqS&ust=1608330410265000&source=images&cd=vfe&ved=0CAIQjRxqFwoTCLCMqe-H1u0CFQAAAAAdAAAAABAJ
Image 2 : original from instructor’s simulink model

## Slide 9: About the Course

## Slide 10: Course overview – What?
What do we learn in this course ?
  Automotive vehicle controls for motion control in autonomous vehicles
  Practical application of control systems to develop Level 2+ ADAS features. (ACC + LCA + Autopilot)
  Model based design and implementation
1

## Slide 11: Course overview – How?
How do we do it?
  Understand dynamics and control systems
  Model algorithms using MATLAB / Simulink
  Improve algorithms to add various functionalities to the feature
Notes: Image 1 : original screenshot
Image 2 : https://www.google.com/url?sa=i&url=http%3A%2F%2Fmehanizacija.ftn.uns.ac.rs%2Fwp-content%2Fuploads%2F2017%2F07%2FPart-12.pdf&psig=AOvVaw0GU5_9Q23kzMZ7PTJBvi1R&ust=1608330761936000&source=images&cd=vfe&ved=0CAIQjRxqFwoTCMDAhJeJ1u0CFQAAAAAdAAAAABAE

## Slide 12: Course overview – why?
Why are we learning this?
  ADAS systems are the fastest growing segment in automotive electronics
  Every OEM is fighting to the top for better autonomous vehicle technology
  Extremely cool tech to build smarter vehicles

## Slide 13: Prerequisite for this course
Hardware and Software tools:
  MATLAB version preferably 2018b and above
  Control system toolbox in MATLAB
  Autonomous vehicle toolbox in MATLAB
  Compatible PC requirements for MATLAB 2018b

## Slide 14: Prerequisite for this course
Theory and background:
  Linear algebra
  Classical control systems basics
  General knowledge about vehicle components and dynamics

## Slide 15: Automotive control systems

## Slide 16: Powertrain Controls
Engine
Transmission
EGR
Throttle control
Spark control
Notes: Instructions : create an image of the car and show the red boxes pointing to the engine, transmission

## Slide 17: Vehicle Controls
ABS / brake controls
Steering control
Cruise control
Notes: Instructions : create an image of the car and show the green boxes pointing to the steering, brakes

## Slide 18: Body Control
Mirrors
Head lamps
Doors / Roof
Notes: Instructions : create an image of the car and show the purple boxes pointing to the mirrors, headlight and doors

## Slide 19: System Modelling

## Slide 20: System modeling basics
Every dynamic system can be modelled into spring mass damper systems.
System modeling generates mathematical equations that can used to calculate control variables.
2
Image to be replaced with a recreated one.

## Slide 21: System modeling example
3

## Slide 22: Control System

## Slide 23: Control systems basics
Controller
(ECU computer)
Actuator / Plant
(powertrain throttle body)0
Sensor
(wheel speed sensor)
Actual output
(actual speed)
Desired output
Ex: cruise speed
+-
Measurement
Comparison
Computation
Correction
Notes: Image 3 : car with speed 25mph. Image to be created should be a car with a vehicle speed on top.

## Slide 24: Laplace domain
TRANSFER FUNCTION

## Slide 25: Laplace domain table

## Slide 26: S domain example in Simulink
Notes: A : the arrow for F force should be going the other side.

## Slide 27: Classical control analysis
Control systems are designed to meet the following criteria
Stability
Transient performance
Disturbance rejection
Robustness
Control magnitude criteria
5
3
4
2
1
5
Notes: Image 1 : need a rocket image to show unstability to match other examples

## Slide 28: Stability
Properties of a stable system:
  Initial condition response decays to zero as time goes to infinity
  The forced response remains bounded when the input is bounded
  Output decays to zero once input is turned off
6

## Slide 29: Example in MATLAB
Root locus showing poles and zeros of a stable LTI system
Stable LTI system
Unstable LTI system

## Slide 30: Root locus conclusion after demo
It is the locus of the roots of the characteristic equation by varying system gain K (usually proportional gain)from zero to infinity
  As poles move up and down the imaginary axis the oscillating frequency increases
  As poles move to the left along the real axis the rate of exponential decay increases
  As poles move right of the imaginary axis rate of exponential growth increases (unstable)

## Slide 31: Transient Performance

## Slide 32: Transient performance

## Slide 33: Transient performance specifications

## Slide 34: Formulas for transient response specifications
Time Domain Specification | Formula
Delay Time | 
Rise Time | 
Peak Time | 
4
ઠωn
4
ઠωn
%Peak Overshoot | 
Setting time for 2% tolerance band | ts =

## Slide 35: Transient performance : First order pole system
7

## Slide 36: First order practical example
Observe low pass filter example in MATLAB

## Slide 37: First order Continued

## Slide 38: Transient performance : Second order pole system
Image to be recreated

## Slide 39: Second order example in MATLAB
%Mp = 8.1%
Tr = 0.296s
Ts = 1.03s
0 0.5 1 1.5 2 2.5
0.3
0.25
0.2
0.15
0.1
0.05
0
Time (seconds)
Amplitude
Step response

## Slide 40: System Types

## Slide 41: Steady state error
Steady-state error is defined as the difference between the input (command) and the output of a system in the limit as time goes to infinity.
Note: Steady state error analysis is only useful for stable system.

## Slide 42: System Type
System type tells us how a transfer function will respond in steady state with respect to an input (reference input or disturbance input).
Example let’s say we have a Type 1 system with respect to R.(by hand).

## Slide 43: How to analyze system type

## Slide 44: System type summary
System type helps to determine whether the steady state error is 0, finite, or infinite for a particular input (step, impulse, parabola etc.).
System type can be increased by adding an integrator to a controller.
Steady state error results involving system type apply only to unity feedback systems. Non unity feedback systems resolve into unity systems and then solve them.

## Slide 45: Disturbance rejection and tracking

## Slide 46: Disturbance rejection and tracking
Disturbance rejection analysis is the ability of a closed loop system to ignore external disturbances. (Ex: wind turbulence on rocket, down hill in cruise control)
Tracking analysis is a measure of how closely a system output follows reference input
We will study this closely during lateral control lectures
Wind as disturbance

## Slide 47: Disturbance rejection and tracking analysis with step inputs (hand calculation)

## Slide 48: Disturbance rejection and tracking analysis with step input

## Slide 49: Other common controls concepts to consider
Control magnitude
  Must be within system limitations
  Ex: Rocket engine has limited thrust capacity hence the control input cannot cross above that. (ex: max thrust 6806kN)
Robustness :
  A system is robust if the performance specifications are met in the presence of parameter variations within defined range.
  Ex: The rocket control system must be able to operate in different payloads within defined range. (ex: 22800 kg +/ 5500 kg)
SpaceX falcon 9 has a payload capacity of 22800 kg expandable to +5500 for geostationary orbits.
SpaceX falcon 9 has a maximum thrust capacity of 6806kN at liftoff
Notes: Image source https://pixabay.com/photos/rocket-launch-rocket-space-shuttle-67649/

## Slide 50: PID Controller

## Slide 51: PID Controller
PID controller algorithm: Proportional (P); Integral (I); Derivative (D)
  P = depends on the present error
  I = accumulation of past errors
  D = prediction of future errors
PID used in throttle body
8
PID used in robotics
9
PID used in automation
10
PID used in ADAS

## Slide 52: PID Controllers

## Slide 53: Building a PID system in Simulink
Consider the mass spring damper example and model in Simulink
Mass = 1kg;
K = 10 N/m;
B = 20 Ns/m
To be recreated

## Slide 54: PID controllers summarized
Proportional:
  Speeds up the response (reduces rise time)
  As Kp increases
    %Mp overshoot increases (oscillations increases)
    pushes system towards instability
  Improves steady state tracking
Time
Amplitude

## Slide 55: PID controllers summarized
PD (Proportional plus derivative):
  PD control adds sort of a damping.
  Disturbance rejection and tracking may be improved.
  Large derivative gains are often difficult to realize in proactive due to large sensor noise
Time
Amplitude

## Slide 56: PID controllers summarized
Proportional plus integral (PI) :
  PI control can improve both disturbance rejection and tracking performance
  Large integral gains can make the system go unstable, usually more easily than a simple P controller
  PI control may result in larger settling time and high overshoot. (also sometimes known as integrator wind-up error)
Time
Amplitude

## Slide 57: PID controllers summarized
Proportional integral and derivative (PID):
  Tracking & disturbance rejection is usually better due to integral term
  Derivative gains may need to be made lower than theoretical values due to sensor noise
  PID tuning is a tricky process. There are several ways like Trial and error , Ziegler-Nichols, twiddle algorithm
Amplitude
Time

## Slide 58: Rule of thumb with PIDs
Gain Values | Rise time | Overshoot | Settling time | Ess
Kp | Decrease | Increase | Small change | Decrease
Ki | Decrease | Increase | Increase | Decrease
Kd | Small Change | Decrease | Decrease | No change

## Slide 59: PID auto tuning with Twiddle algorithm
Twiddle is an optimization algorithm that tries to find a good choice of parameters p for an algorithm A that return an error
Use trial and error to determine parameter vector P and initialize twiddle algorithm
Follow the iterative process to make small value change either positive and negative & If there is improvement the change is kept until the error is below the threshold

## Slide 60: PID auto tuning with Twiddle algorithm
To be recreated

## Slide 61: Summary
This week, we learned
  About the controls of autonomous vehicles
  How the system the system is modelled
  The control system of autonomous vehicle
  How a system type is analyzed
  How disturbances from the surroundings are tackled
  Relevance of PID controllers

## Slide 62: Image Credits
Ian Maddox, CC BY-SA 4.0 <https://creativecommons.org/licenses/by-sa/4.0>, via Wikimedia Commons
Yapparina, CC0, via Wikimedia Commons
No machine-readable author provided. Ilmari Karonen assumed (based on copyright claims)., Public domain, via Wikimedia Commons
Olivier Cleynen and Werneuchen, CC0, via Wikimedia Commons
NASA/Joel Kowsky, Public domain, via Wikimedia Commons
Pasimi, CC BY-SA 4.0 <https://creativecommons.org/licenses/by-sa/4.0>, via Wikimedia Commons
Inductiveload, Public domain, via Wikimedia Commons
Magnus Bäck, Public domain, via Wikimedia Commons
Eirik Refsdal from Trondheim, NORWAY, CC BY 2.0 <https://creativecommons.org/licenses/by/2.0>, via Wikimedia Commons
Phasmatisnox, CC BY 3.0 <https://creativecommons.org/licenses/by/3.0>, via Wikimedia Commons

## Slide 63: THANK YOU